## Slide 1: Multi-scanner Harmonization of Paired Neuroimaging Data via Structure Preserving Embedding Learning Mahbaneh Eshaghzadeh Torbati1, Dana L. Tudorascu1, Davneet S. Minhas1, Pauline Maillard2, Charles S. DeCarli2, Seong Jae Hwang1 1University of Pittsburgh, 2University of California, Davis
Mahbaneh Eshaghzadeh Torbati | mae82@pitt.edu Dana L. Tudorascu | dlt30@pitt.edu Davneet S. Minhas | minhasd@upmc.edu Pauline Maillard | pauli.maillard@gmail.com Charles S. DeCarli | cdecarli@ucdavis.edu Seong Jae Hwang | sjh95@pitt.edu
  This work was supported by the following NIH/NIA grants: R01 AG063752 (D.L. Tudorascu), P30 AG10129 and UH3 NS100608 (C. DeCarli), and the University of Pittsburgh Alzheimer’s Disease Research Center Grant P30 AG066468 (S. Hwang).
  Reference:
  [1] Kenichi Oishi, et al. Atlas-based whole brain white matter analysis using large deformation diffeomorphic metric mapping: application to normal elderly and alzheimer’s disease participants. Neuroimage, 2009.
  [2] Y Zhang, et all. Segmentation of brain MR images through a hidden markov random field model and the expectation-maximization algorithm. IEEE Trans Med Imaging, 2001.
Background
Results 1: Image Similarity
  Combining datasets from multiple sites/scanners has been becoming increasingly more prevalent in modern neuroimaging studies.
  Problem: Despite benefits from growth in sample size by combining datasets, substantial variability associated with site/scanner-related effects exists which may inadvertently bias down-stream analyses (Figure 1).
  Harmonization is the task of removing scanner effects directly from image-derived measures (image-level harmonization) or the images (image-level harmonization).
  Figure 1. Example of scanner effects.
  In this work, we:
    introduce the first paired multi-scanner data on four different scanners.
    propose a multi-scanner deep harmonization framework called MISPEL (Multi-scanner Image harmonization via Structure Preserving Embedding Learning).
Methods | SSIM Between Scanners |  |  |  |  | 
Methods | GE-Philips | GE-Prisma | GE-Trio | Philips-Prisma | Philips-Trio | Prisma-Trio
RAW | 0.75 (0.04) | 0.78 (0.04) | 0.78 (0.05) | 0.81 (0.03) | 0.81 (0.03) | 0.87 (0.04)
MISPEL | 0.84 (0.04) | 0.85 (0.04) | 0.86 (0.05) | 0.87 (0.03) | 0.87 (0.03) | 0.91 (0.03)
Contributions
Paired Multi-scanner Dataset
Results 2: Volumetric Similarity
  Figure 2. Paired multi-scanner dataset.
Method: MISPEL
  Acquisition: 18 subjects scanned on 4 different scanners with short delay (Figure 2).
  Preprocessing:
    Non-linear registration to a T1-Weighted image atlas [1].
    Spatial intensity inhomogeneity correction.
    Skull stripping.
    Scaling.
    These preprocessed images are referred to as RAW images and are input images for harmonization.
  MISPEL: an image-level harmonization to preserve the structure of images.
  Notations and loss functions:
  Data: N axial slices (combined across all subjects) from each of M scanners.
  Variables:
  : Scanner and slice index, respectively
  : Embedding’s component index
  , : Max iteration for Steps 1 and 2
  : Axial slice from scanner
  : Latent embedding of
  : Latent embedding of
  : index for elements in
  : Harmonized
  Networks:
  : Encoder U-Net for
  : Decoder linear map for
  Loss functions:
  +
  MISPEL Training Algorithm:
  1: Procedure Step 1: Embedding learning
  2: for or until do
  3: for each slice do
  4: for each scanner do
  5:
  6:
  7: end for
  8: Update and
  using
  9: end for
  10: end for
  11: end procedure (end Step 1)
  12: procedure Step 2: Harmonization
  13: for or until do
  14: for each slice do
  15: for each scanner do
  16:
  17:
  18: end for
  19: Update only using
  20: end for
  21: end for
  22: end procedure (end Step 2)
Acknowledgments
  Scanner effects exist in our in-house paired multi-scanner dataset.
  MISPEL succeeded in harmonization of our data evaluated on image and volumetric similarity.
Conclusions
  Figure 3. GM volumes.
  Figure 4. WM volumes.
  Experiment: Studying scanner effects and MISPEL harmonization on volumes of gray matter (GM) and white matter (WM) tissue types extracted by FSL FAST segmentation [2].
  Scanner effects appeared as dissimilarity of distributions
  Table 1. Mean (standard deviation) of SSIMs within pairwise combinations of scanners.
  Experiment: Comparing the similarity of RAW and MISPEL-harmonized images within pairwise combinations of scanners, using the structural similarity index measure (SSIM).
  The scanner effects were partially removed by images getting more similar (increased SSIMs) after the MISPEL harmonization (Table 1).
  distributions of both tissues across scanners. Harmonization happened as distributions got more similar to each other (Figures 3 and 4).